## Slide 1: PCB Basics using Altium Designer
ITLP Skill Building Workshops Spring 2025
Level 1:
Notes: Does any one know what a PCB is? Printed Circuit Board – how we electrically connect components on one device
In this workshop we will learn about schematics, PCB layout, and manufacturing files
In level 2 you can learn how to create your own components using datasheets and resources online and custom boards

## Slide 2: Printed Circuit Artwork

## Slide 3
First Day!
ITLP Announcements
1
7
8
9
10
11
12
2
3
4
5
6
13
14
15
16
Finals
What week are we in?
Fall Break!
Last Day!
CU Holiday!
EXPO!
Workshop Sign Up Online
ITL Program Centers
Launch Point
Project Depot
Project Vault
Manufacturing Center
ITL Program People
Electronics Center
Electronics Fabrication Center
Notes: But before we jump into [insert workshop here] content, I just want to briefly remind you about the ITL Program offerings.
We are at Week [1-15] in the semester, and that means we have [15-1 ]weeks until your project expo!
This means you have [15-1] weeks left to complete mandatory out of class workshops. For example, saws and drills, which will no longer be available after week 4 [FALL 2022] .
I am here to be your workshop instructor in class today, but the ITL Program hosts hundreds of after-hours workshops to help you get a jumpstart on your hands-on engineering projects. Some of which get you access to amazing equipment and spaces, others are just awesome skills you might want to support your projects.
Just a reminder, as you move into prototyping and manufacturing season we have :
1.We have two electronics centers for basic electronic support and advanced/PCB support (can design and make your own PCB)
2.We have a manufacturing center where you can use wood tools or metal tools (like mills, lathes, and CNC machines)
3.We have 5 laser cutters, about 15 3D printers
4.A project depot with openly available tools
5.And a consumables closet, where there is a bunch of free supplies that you can use for your projects.
Most of all though, we have six engineers, two machinists, many support students (look for the navy blue vests) staffed in the ITL Program, whose main priority is to provide excellent support to students and faculty, so be sure to come ask us questions!

## Slide 4: ITLP Workshop Learning Goals
Learning Objective 1:
Learning Objective 2:
Learning Objective 3:
Know the steps to make a PCB in the ITL Program.
Use the provided files to create a PCB design.
Export the files needed to manufacture a custom printed circuit board.

## Slide 5: ITLP PCB Manufacturing
Put parts on your board; depending on type of manufacturing this will use different equipment in the lab.
Step 3
Assembly
Following your DFM approval, the engineer will set you up with a manufacturing appointment. This is where we lead you through manufacturing your PCB.
Step 2
Manufacturing
This is a Design For Manufacturing(DFM) review; while we often help validate designs, this is more about determining if we can manufacture in-house than if your design will function.
Step 1
Design Review
Notes: Step 0 – Designing your PCB on your own (Taking the workshop)
Step 1 – Design review with Lauren to talk about your PCB and any flaws it may have
Step 2 – Manufacture PCB with the equipment we have at the ITLL
Step 3 – Assemble all electronic components onto the board to make it functioning

## Slide 6: ITLP PCB Manufacturing
ITLL PCB Manufacturing Portal Link
Select Single-Sided or Double-Sided Copper Clad FR4 Substrate
Drill any holes needed for through hole parts or vias
Mill unwanted copper from surface
Notes: Material we have is FR4 (two sided with dialectric in middle, single sided)
Our process is a subtractive process. We drill holes for any components specified in the schematic
Then we mill the unwanted copper away from the board to leave copper traces (like wires) on the board

## Slide 7: Designing a PCB
Step 1
The Schematic
Step 3
Gerber File Generation
Step 2
The PCB Layout
Notes: Make shcematic
Make PCB layout, where we lay/map out all components on board specified from our schematic
Then generate gerber files to manufacture the PCB (we can think of these similar to gcode files for 3D printing)
Helps the machines manufacturing understand where to drill holes and mill out traces

## Slide 8: Download Altium Project Folder
itll.ws/ECAD
  ECAD
    Level 1
Download “Altium_PCB_Project.ZIP”
Extract contents to desktop
  Right click > Extract All…
    Save to Desktop
Double-click file “Altium_PCB_Project.PrjPcb”

## Slide 9: Open Altium Designer
If using Lab Station Computers
1) Open the start menu (windows key)
2) Search Altium Designer
3) Should see page “Welcome Guest”
If working on Checkout Laptops
1) Sign in to CU VPN
2) Open Altium Designer
3) Click “Not Signed In” (top right corner)
4) Click “Licenses”
5) Click “Connect to Server” – “Ok”
6) Click “Use License” (at bottom)
7) Should see “Release”
Notes: Log in to computers – google – link
Really important that you save to desktop and extract all files

## Slide 10: Making New Project
Click on “File” (top Left)
Create “New” > “Project”
- Make sure to save in Desktop
- Name your Project!!
Once Project is Created…
Click “File” > “New” > “Schematic”
Save in Desktop!!!!
Notes: Log in to computers – google – link
Really important that you save to desktop and extract all files

## Slide 11
Everything will exist in your “Projects” panel on the left side of your screen

## Slide 12: Uploading Libraries
itlp.link/WorkshopResources
  ECAD
    Libraries
Download “GEEN3010_Stoplight_SP2026”
Drag Library into Altium
  Click Install
    Open Components Window
Should see New Stoplight Library
Notes: Log in to computers – google – link
Really important that you save to desktop and extract all files

## Slide 13
The process of getting parts from your breadboard or prototype into digital space
Schematic Capture

## Slide 14
Double-click “Schematic.SchDoc” to open the schematic page

## Slide 15: Navigating the Schematic
Shift + Mouse Scroll
Mouse Scroll
Ctrl + Mouse Scroll
Right-Click

## Slide 16: Place Parts
Using the Heads-Up Toolbar, select the Place Part Tool
  ”Place Part”
The Components Panel will appear on the right →
Click the dropdown menu
  Select “ITLProgram_PCB_Basics_SP2025.IntLib”

## Slide 17: The Hottest of Keys
Open Part Properties
Rotate Part while active on cursor (picked up on the mouse!)

## Slide 18: Components
Carry 3 Important Pieces of Information
The Symbol
The Footprint
The 3D Model*

## Slide 19: Populate the Timer
1 x ATtiny85 IC

## Slide 20: Populate the Regulator
1 x LM7805 Voltage Regulator

## Slide 21: Populate the Resistors
3 x 330 Ohm (SMD)
1 x 10k Ohm (THT)

## Slide 22: Populate the Capacitors
1 x 0.33 uF
1 x 0.1 uF

## Slide 23: Populate the LEDs
3 x 5mm
  Green
  Yellow
  Red

## Slide 24
Components
Polarized vs Unpolarized
Unpolarized
Polarized

## Slide 25: Populate the Power Port
1 x 9V Snap Connector

## Slide 26: Populate the Push Button
1 x Push Buttton

## Slide 27: Populate the Switch
1 x Toggle Switch

## Slide 28
Progress So Far

## Slide 29: The Symbol
Reference Designator
Value or Part Number

## Slide 30: The Symbol
Moving Symbol
Moving Reference Designator
Moving Value
Notice the Green Box relocates based on if you have selected symbol, reference designator, or value/part

## Slide 31: Annotate Power & Ground
Using the Heads-Up Toolbar, select the Place GND Power Port Tool
  “Place GND Power Port”
Place 5 GNDs across the bottom
Right-click to show more options
Place 1 VCC at the top
GND
VCC

## Slide 32: Schematic Etiquette
POWER
INPUTS
OUTPUTS
GROUND
CONTROLLER
Order of Operations

## Slide 33: Schematic Etiquette
Build the Network of Connections
Spam Escape

## Slide 34: Schematic Etiquette
Tool-sception
hit escape at least 3-4 times

## Slide 35
Schematic Etiquette
Legacy ECAD Programs

## Slide 36
No Nodes on Pins
No 4-Way Junctions
No Pins on Pins
Schematic Etiquette
Routing
Notes: No nodes on pins. Blue dot on node of component is bad etiquette – want a little bit of wire in between. Older programs used to cause error
No 4 way junctions. 4 components connected at one center node
No components wired directly together

## Slide 37
No Wires Overlapping Components
Schematic Etiquette
Routing

## Slide 38: Wired Schematic
Final Design

## Slide 39: Annotate the schematic
Add Values to Resistors, Capacitors, LEDs by selecting the word value and editing the word value.

## Slide 40: Verify Values

## Slide 41: Annotate the Schematic
Tools (Menu Bar)
  Annotation
    Annotate Schematics…

## Slide 42: Automatically Annotate Schematics
UPDATE CHANGE LIST
  OKAY!
Engineering Change Order (ECO)
  Validate
  Execute
  Close
Close

## Slide 43: Validate Project

## Slide 44: Final Schematic! (Save your work here)

## Slide 45
SAVE​
SAVE​ NOW
REALLY, SAVE​
SAVE​, PLEASE

## Slide 46: PCB Layout
The process of taking your schematic content and generating the artwork used to manufacture printed circuit boards.

## Slide 47
This is the pcb layout workspace, here is where artwork generation begins. The purpose of a pcb is to execute the requirements of your schematic. This is your final product and often has constraints around size.
HEADS UP Toolbar
Double Click

## Slide 48: Bring in Content from Schematic
File Menu Bar
  Design>
    Import Changes from …
Engineering Change Order
  Select VALIDATE in lower left corner
  Select EXECUTE in lower left corner
  Close

## Slide 49: Zoom out to see components

## Slide 50: Rearrange Components
Space Bar still rotates components.
GOAL: FEWEST crossing little yellow lines.

## Slide 51: Route the Physical Copper Tracks
Hotkey: ctrl + w
Blue lines/bottom layer tracks only

## Slide 52: Finalize Board
Place Ground Pour

## Slide 53: Select New Polygon from… BOARD OUTLINE

## Slide 54: Change NET and LAYER

## Slide 55: Board View Modes

## Slide 56: Create CAM files
File > Fabrication Outputs > Gerber Files
File > Fabrication Outputs > NC Drill Files

## Slide 57: Gerber Setup
Plot Layers Drop Down > Select Used
Apply

## Slide 58: Generate Gerber Files
CHANGE OUTPUT FILE LOCATION

## Slide 59: NC Drill Files
Okay >
Okay >

## Slide 60: Generate Drill Files
CHANGE DEFAULT STORAGE

## Slide 61: Workshop Survey
Learning Objective 1
Know the steps to make a PCB in the ITL Program.
Learning Objective 2
Use the provided files to create a PCB design.
Learning Objective 3
Export the files needed to manufacture a custom printed circuit board.
itlp.link/ws11